## Slide 1
Select fill hole to fill the holes.
Shown on the left is a dyna model with and without Fill hole option.
Without fill hole
With fill hole
Always select one node from the curvature of the top surface of the weld.
A patch is default for Pamcrash solver profile.
If Patches are required for Abaqus and Dyna profiles , Please select Patch-ABDYN tickbox.
Selection Mechanism
Weld Circular
Enter a component name for joint .
Enter a component ID for joint component leave an interval of 10 from previous ID(interval 10)

## Slide 2
The patches will be along the normal of The elements for Doghouses .Tick the Face normal check box to take control
Of the direction.
Doghouse
Without face normal on blue face
With face normal on blue face
Select fill hole to fill the holes.
Shown on the left is a dyna model with and without Fill hole option.
Select joint on slave to create special type of rigid connection. An extended slave branch that connects with joint.
1.4mm
Type in the final joint length required to override the default values.
Doghouse Ext
Doghouse
Always select one node from the inner curvature at the top surface of the Doghouse.
Selection Mechanism

## Slide 3
Doghouse (Continued)
With face normal on blue face
Change El Types from rigids to beams to change type of connection. Default is rigids for all solvers.
Patch Translate 8mm
Patch Radius 14mm
Input the Patch radius and Patch translate values for defining the patch translation values and Patch radius values.
Tick patch all to connect all nodes of the patch to rigid body .
By default , only the inner edge nodes of the patch are connected to rigid body.

## Slide 4
Doghouse (Continued)
Input the Patch radius and Patch translate values for defining the patch translation values and Patch radius values.
C3-R Radius - 12
C2-R Radius - 8
C1-R Radius - 6
Option to specify Dia and Thickness for the patch.
For Pamcrash nodal thickness is defined.
For other solvers- at the moment 1mm constant thickness
C3-T Thickness - 4
C2-T Thickness - 3
C1-T Thickness - 2
Enter a component name for joint .
Enter a component ID for joint component leave an interval of 10 from previous ID(interval 10)
Selection Mechanism

## Slide 5
Weld Ribs
Use Face normal and Tolerance input boxes to control the direction and distance of nodes that needs to be added to the rigids or beams group.
Select Weld ribs to create weld rib modelling.
Enter a component name for joint .
Enter a component ID for joint component leave an interval of 10 from previous ID(interval 10)
Selection Mechanism

## Slide 6
Locator
Select locator create locator connections.
Tick the face normal if the normal of
element of node selected is positive (Red) .
Use Face normal and Tolerance input boxes to control the direction and distance of nodes that needs to be added to the rigids or beams group.
Enter a component name for joint .
Enter a component ID for joint component leave an interval of 10 from previous ID(interval 10)
Selection Mechanism